## Slide 1
ABNORMALITY REPORT — RCA & CAPA/PAA
Feed Charge Pump PU-2101B
Mechanical Seal Leakage
AR NUMBER
AR-2026-ARP-0117
TAG / PLANT
PU-2101B | ARP
DATE OCCURRENCE
12 Mar 2026
PRE-RISK
III (Score 200)
PIC (RCA)
REL-05
Procedure No. RCA-P-0050-03 • Form RCA-F-0075-02
Equipment Related Risk

## Slide 2
PROBLEM IDENTIFICATION
AR Details & Problem Statement
02/11
AR IDENTIFICATION
Title / Problem
Feed Charge Pump PU-2101B — Mechanical Seal Leakage
AR Type
OPEDR (Operation) — Uptime
Plant / Unit
ARP (Aurora Resin Plant)
Tag / Eq. Class
PU-2101B | Class B
Discipline
ROT
Date Occurrence
12 Mar 2026
Date Reported
13 Mar 2026
Immediate Action
Isolate PU-2101B, swap to spare PU-2101A, replace mechanical seal cartridge
SEVERITY
Major
PRE-RISK
III
DOWNTIME
18.5 h
LOSS
$226.44k
PROBLEM STATEMENT
Mechanical seal of Feed Charge Pump PU-2101B failed on 12-Mar-2026, causing seal leakage and an unplanned feed reduction to the ARP reactor section.
RCA & CAPA/PAA | AR-2026-ARP-0117 | PU-2101B — ARP

## Slide 3
GENERAL PROCESS OVERVIEW
Chronology of Events
03/11
11-Mar-2026
ARP produced resin grade PR-5502 (Reactor Rate ± 13.6 T/H). Field operator noted minor seal weep on PU-2101B during routine round.
12-Mar-2026 02:15
Seal flush low-flow alarm annunciated; visible feed seal leak with low suction pressure. Pump auto-tripped on low discharge pressure.
12-Mar-2026 02:40
Feed section reduced; charge to reactor curtailed pending seal repair. Rotating team mobilized.
12-Mar-2026 09:20
Seal cartridge & shaft sleeve inspected — seal faces heat-checked / worn (dry-running signature).
12-Mar-2026 20:45
New seal cartridge installed, pump commissioned, feed restored to ± 13.6 T/H.
Problem: Mechanical seal of Feed Charge Pump PU-2101B failed on 12-Mar-2026, causing seal leakage and an unplanned feed reduction to the ARP reactor section.
RCA & CAPA/PAA | AR-2026-ARP-0117 | PU-2101B — ARP

## Slide 4
ASSESS
Past Performance Analysis
04/11
HISTORICAL DATA & EVIDENCE
PU-2101B seal MTBF trended down from 26 to 9 months over the last 3 cycles. Seal-flush flow had been intermittently below the 6 L/min design minimum during feed swings, indicating recurring dry-run exposure.
IMPACT SUMMARY (4W)
What:
Mechanical seal of PU-2101B leaked / failed
When:
12-Mar-2026 (02:15)
Scope:
Reduced charge feed to ARP reactor section
Uptime Loss:
18.5 hours → 251.6 ton → $226.44k
RCA & CAPA/PAA | AR-2026-ARP-0117 | PU-2101B — ARP

## Slide 5
TARGET SETTING
Actual vs Target Condition
05/11
ACTUAL CONDITION (Before Improvement)
Feed reduction due to PU-2101B mechanical seal leak
TARGET CONDITION (Project Y)
No unplanned feed reduction due to PU-2101B seal failure (seal MTBF ≥ 24 months)
TARGET METRIC
Recurrence of this equipment failure mode:
Before = 1 case → Target = 0 case
Chart: Failure Case — Before vs Target
| Before | Target
Failure Cases | 1 | 0
RCA & CAPA/PAA | AR-2026-ARP-0117 | PU-2101B — ARP

## Slide 6
ROOT CAUSE ANALYSIS
Parameter Verification (4P)
06/11
#
Problem Phenomenon / Parameter
Result
Evidence / Finding
P1
Pump operated above rated flow
G
Operated at 13.1–13.7 T/H vs rated max 18 T/H — within limit.
P2
Suction pressure below NPSH margin
NG
Suction pressure dropped during feed swing; NPSH margin < 0.5 m (spec ≥ 1.0 m) — cavitation risk.
P3
Seal flush flow below minimum
NG
Seal-flush flow measured 3–4 L/min vs 6 L/min minimum — seal ran dry intermittently.
P4
Cooling water to seal cooler inadequate
G
Seal cooler outlet temp normal (42 °C) — cooling adequate.
P5
Seal faces beyond service life
G
Seal in service 11 months, within 24-month design life.
NG = current condition not meeting standard (problem) • G = meets standard
RCA & CAPA/PAA | AR-2026-ARP-0117 | PU-2101B — ARP

## Slide 7
ROOT CAUSE ANALYSIS
4M + 1E Verification
07/11
#
Man / Machine / Method / Material / Environment
Result
Evidence / Finding
X1
No low-NPSH / flush-flow interlock in DCS
NG
No automatic trip or alarm on loss of seal-flush flow.
X2
Feed-swing SOP allows fast rate ramp
NG
SOP permits > 2 T/H per minute ramp, driving suction transients.
X3
PM covers seal only, not flush system
NG
Seal-flush plan (Plan 11) not on the PM check-sheet.
X4
Operator competency on seal-flush monitoring
G
Operators trained; no competency gap identified.
ROOT CAUSE: Premature mechanical seal failure caused by intermittent dry-running: suction cavitation during feed swings reduced NPSH and seal-flush flow dropped below the 6 L/min minimum, with no interlock to protect the seal.
RCA & CAPA/PAA | AR-2026-ARP-0117 | PU-2101B — ARP

## Slide 8
RCA — MATRIX PRIORITY
Impact vs Control Prioritization
08/11
X1 X2 X3
P2 P3
Low
Medium
High
IMPACT →
CONTROL →
Low
Medium
High
Prioritized root causes (high impact) are addressed first via Corrective & Pro-Active Actions →
RCA & CAPA/PAA | AR-2026-ARP-0117 | PU-2101B — ARP

## Slide 9
IMPROVE
Corrective & Pro-Active Action (CAPAA)
09/11
RC
Corrective Action
Plan Date
PIC
Status
P3
Install seal-flush flow switch with DCS alarm on PU-2101B
24-Apr-2026
REL-05
In Progress
X1
Add low-NPSH / loss-of-flush trip interlock in DCS
24-May-2026
REL-02
Open
PRO-ACTIVE ACTION (roll-out to similar equipment)
RC
Pro-Active Action
Plan Date
PIC
Status
P3
Roll out flush-flow switch to PU-2101A spare
24-May-2026
REL-05
Open
X1
Apply interlock standard to all API-682 seal pumps in ARP
24-Jul-2026
REL-02
Open
RCA & CAPA/PAA | AR-2026-ARP-0117 | PU-2101B — ARP

## Slide 10
IMPROVE
Preventive & Risk Analysis
10/11
PREVENTIVE / PRO-ACTIVE ACTION (Good Condition Parameters)
Item
Possible Root Cause
Preventive Action
Plan Date
PIC
P2
Suction cavitation
Revise feed-swing SOP to cap ramp at 1 T/H per minute
24-Apr-2026
ROT-01
X3
Flush system not in PM
Add seal-flush system (Plan 11) to PU-2101B PM check-sheet
24-Apr-2026
REL-05
RISK ANALYSIS OF CORRECTIVE ACTION
Corrective Action
Potential Risk
Countermeasure
Plan Date
PIC
Install flow switch & interlock
Nuisance trips during commissioning
Stage commissioning with bypass timer & operator brief
24-May-2026
REL-05
PM SCHEDULE ESTABLISHED
PM No.
Description
Group
Interval
PM-1
Weekly seal-flush flow & seal-pot level check PU-2101B
Rotating
Weekly
PM-2
Quarterly seal condition & shaft run-out inspection
Rotating
3-monthly
RCA & CAPA/PAA | AR-2026-ARP-0117 | PU-2101B — ARP

## Slide 11
Downtime & Closure Summary
DOWNTIME
18.5 h
PRODUCTION LOSS
251.6 ton
ESTIMATED LOSS
$226.44k
PRE-RISK
III (200)
ROOT CAUSE
Premature mechanical seal failure caused by intermittent dry-running: suction cavitation during feed swings reduced NPSH and seal-flush flow dropped below the 6 L/min minimum, with no interlock to protect the seal.
KEY CORRECTIVE / PRO-ACTIVE ACTIONS
• Install seal-flush flow switch with DCS alarm on PU-2101B
• Add low-NPSH / loss-of-flush trip interlock in DCS
• Revise feed-swing SOP to cap ramp at 1 T/H per minute
AR-2026-ARP-0117 • PU-2101B — ARP