## Slide 1
ABNORMALITY REPORT — RCA & CAPA/PAA
Equipment Related Risk
Cracked Gas Compressor KO-3201
High Radial Vibration Trip (Bearing Distress)
AR NUMBER
AR-2026-ZCU-0142
TAG / PLANT
KO-3201 | ZCU
DATE OCCURRENCE
29 Apr 2026
PRE-RISK
II (Score 4000)
PIC (RCA)
REL-05
Procedure No. RCA-P-0050-03 • Form RCA-F-0075-02

## Slide 2
PROBLEM IDENTIFICATION
AR Details & Problem Statement
02/11
AR IDENTIFICATION
Title / Problem
Cracked Gas Compressor KO-3201 — High Radial Vibration Trip (Bearing Distress)
AR Type
OPEDR (Operation) — Uptime
Plant / Unit
ZCU (Zeta Cracker Unit)
Tag / Eq. Class
KO-3201 | Class A
Discipline
ROT
Date Occurrence
29 Apr 2026
Date Reported
30 Apr 2026
Immediate Action
Controlled shutdown of compression train, replace DE journal bearing, flush lube-oil system
SEVERITY
Catastrophic
PRE-RISK
II
DOWNTIME
32.0 h
LOSS
$1584.0k
PROBLEM STATEMENT
Cracked Gas Compressor KO-3201 tripped on high-high radial vibration on 29-Apr-2026 due to journal-bearing babbitt distress driven by water-contaminated lube oil.
RCA & CAPA/PAA | AR-2026-ZCU-0142 | KO-3201 — ZCU

## Slide 3
GENERAL PROCESS OVERVIEW
Chronology of Events
03/11
27-Apr-2026
ZCU compression train running normal; KO-3201 drive-end (DE) radial vibration trending up (from 28 to 52 micron over 5 days).
29-Apr-2026 06:40
KO-3201 DE vibration reached high-high setpoint (75 micron); machinery protection system tripped the compressor.
29-Apr-2026 08:10
Plant rate cut to minimum; lube-oil sample taken — water content 1,800 ppm (spec < 500 ppm).
29-Apr-2026 18:00
DE journal bearing removed — babbitt wiped/distressed. Lube-oil cooler tube leak confirmed.
30-Apr-2026 14:40
New bearing installed, lube-oil system flushed, cooler tube plugged, train restarted to 55 T/H.
Problem: Cracked Gas Compressor KO-3201 tripped on high-high radial vibration on 29-Apr-2026 due to journal-bearing babbitt distress driven by water-contaminated lube oil.
RCA & CAPA/PAA | AR-2026-ZCU-0142 | KO-3201 — ZCU

## Slide 4
ASSESS
Past Performance Analysis
04/11
HISTORICAL DATA & EVIDENCE
KO-3201 DE vibration baseline is 25–30 micron. Trend shows a steady rise over 5 days preceding the trip. Lube-oil water content had drifted above 500 ppm for ~2 weeks without an online alarm.
IMPACT SUMMARY (4W)
What:
KO-3201 tripped on high-high radial vibration
When:
29-Apr-2026 (06:40)
Scope:
ZCU compression train shutdown — full ethylene rate loss
Uptime Loss:
32.0 hours → 1760.0 ton → $1584.0k
RCA & CAPA/PAA | AR-2026-ZCU-0142 | KO-3201 — ZCU

## Slide 5
TARGET SETTING
Actual vs Target Condition
05/11
ACTUAL CONDITION (Before Improvement)
Compressor trip due to bearing distress from contaminated lube oil
TARGET CONDITION (Project Y)
No compressor trip due to lube-oil contamination (water < 500 ppm, vibration < 45 micron)
TARGET METRIC
Recurrence of this equipment failure mode:
Before = 1 case → Target = 0 case
Chart: Failure Case — Before vs Target
| Before | Target
Failure Cases | 1 | 0
RCA & CAPA/PAA | AR-2026-ZCU-0142 | KO-3201 — ZCU

## Slide 6
ROOT CAUSE ANALYSIS
Parameter Verification (4P)
06/11
#
Problem Phenomenon / Parameter
Result
Evidence / Finding
P1
Radial vibration above alarm
NG
DE vibration rose to 75 micron vs 45 micron alarm — bearing distress.
P2
Lube-oil water content above spec
NG
Water content 1,800 ppm vs < 500 ppm spec — film breakdown.
P3
Lube-oil supply pressure low
G
Header pressure 1.8 barg — within normal band.
P4
Bearing beyond service life
G
Bearing in service 3 years vs 6-year design — within life.
P5
Process surge / anti-surge margin
G
Anti-surge margin maintained; no surge event recorded.
NG = current condition not meeting standard (problem) • G = meets standard
RCA & CAPA/PAA | AR-2026-ZCU-0142 | KO-3201 — ZCU

## Slide 7
ROOT CAUSE ANALYSIS
4M + 1E Verification
07/11
#
Man / Machine / Method / Material / Environment
Result
Evidence / Finding
X1
No online water-in-oil monitoring
NG
Water content only checked by weekly grab sample — slow detection.
X2
Lube-oil cooler integrity not trended
NG
No routine cooler tube leak check between TAs.
X3
Vibration alert limits too wide
NG
Alert at 60 micron gave little lead time before 75 micron trip.
X4
Lube-oil purifier not in service
G
Purifier available and operational.
ROOT CAUSE: Journal-bearing babbitt distress caused by degraded oil-film strength from water ingress via a leaking lube-oil cooler tube, undetected due to absence of online water-in-oil monitoring, leading to rising vibration and a high-high trip.
RCA & CAPA/PAA | AR-2026-ZCU-0142 | KO-3201 — ZCU

## Slide 8
RCA — MATRIX PRIORITY
Impact vs Control Prioritization
08/11
X1 X2 X3
P1 P2
Low
Medium
High
IMPACT →
CONTROL →
Low
Medium
High
Prioritized root causes (high impact) are addressed first via Corrective & Pro-Active Actions
RCA & CAPA/PAA | AR-2026-ZCU-0142 | KO-3201 — ZCU

## Slide 9
IMPROVE
Corrective & Pro-Active Action (CAPAA)
09/11
RC
Corrective Action
Plan Date
PIC
Status
P2
Repair leaking lube-oil cooler tube (plug + re-test)
30-Apr-2026
STA-02
Closed
X1
Install online water-in-oil sensor on KO-3201 lube system
30-Jun-2026
REL-05
In Progress
PRO-ACTIVE ACTION (roll-out to similar equipment)
RC
Pro-Active Action
Plan Date
PIC
Status
P2
Retube lube-oil cooler at next TA
31-Oct-2026
STA-02
Open
X1
Apply online water-in-oil monitoring to KO-3202/3203
30-Sep-2026
REL-05
Open
RCA & CAPA/PAA | AR-2026-ZCU-0142 | KO-3201 — ZCU

## Slide 10
IMPROVE
Preventive & Risk Analysis
10/11
PREVENTIVE / PRO-ACTIVE ACTION (Good Condition Parameters)
Item
Possible Root Cause
Preventive Action
Plan Date
PIC
X3
Vibration limits too wide
Tighten KO-3201 vibration alert to 45 micron & shorten trend-review cadence
30-May-2026
REL-05
X2
Cooler integrity not trended
Add lube-oil cooler dP & conductivity trend to reliability dashboard
30-Jun-2026
REL-02
RISK ANALYSIS OF CORRECTIVE ACTION
Corrective Action
Potential Risk
Countermeasure
Plan Date
PIC
Tighten vibration alert to 45 micron
Nuisance alerts on start-up transients
Add start-up alarm suppression timer
30-May-2026
REL-05
PM SCHEDULE ESTABLISHED
PM No.
Description
Group
Interval
PM-1
Weekly lube-oil water-content & particle count
Reliability
Weekly
PM-2
6-monthly lube-oil cooler leak test
Static
6-monthly
PM-3
Continuous vibration trend review KO-3201
Reliability
Daily

## Slide 11
Downtime & Closure Summary
DOWNTIME
32.0 h
PRODUCTION LOSS
1760.0 ton
ESTIMATED LOSS
$1584.0k
PRE-RISK
II (4000)
ROOT CAUSE
Journal-bearing babbitt distress caused by degraded oil-film strength from water ingress via a leaking lube-oil cooler tube, undetected due to absence of online water-in-oil monitoring, leading to rising vibration and a high-high trip.
KEY CORRECTIVE / PRO-ACTIVE ACTIONS
• Repair leaking lube-oil cooler tube (plug + re-test)
• Install online water-in-oil sensor on KO-3201 lube system
• Tighten KO-3201 vibration alert to 45 micron & shorten trend-review cadence
AR-2026-ZCU-0142 • KO-3201 — ZCU