## Slide 1
ABNORMALITY REPORT — RCA & CAPA/PAA
Equipment Related Risk
Feed/Effluent Heat Exchanger HE-3301
High Fouling — Duty Loss & High dP
AR NUMBER
AR-2026-ZCU-0165
TAG / PLANT
HE-3301 | ZCU
DATE OCCURRENCE
21 May 2026
PRE-RISK
III (Score 400)
PIC (RCA)
STA-02
Procedure No. RCA-P-0050-03 • Form RCA-F-0075-02

## Slide 2
PROBLEM IDENTIFICATION
AR Details & Problem Statement
02/11
AR IDENTIFICATION
Title / Problem
Feed/Effluent Heat Exchanger HE-3301 — High Fouling — Duty Loss & High dP
AR Type
OPEDR (Operation) — Uptime
Plant / Unit
ZCU (Zeta Cracker Unit)
Tag / Eq. Class
HE-3301 | Class B
Discipline
STA
Date Occurrence
21 May 2026
Date Reported
22 May 2026
Immediate Action
Isolate HE-3301, bypass via spare train, hydro-jet clean tube bundle
SEVERITY
Moderate
PRE-RISK
III
DOWNTIME
12.0 h
LOSS
$183.6k
PROBLEM STATEMENT
Feed/Effluent Heat Exchanger HE-3301 suffered accelerated tube-side fouling reducing duty and raising dP, forcing an unplanned isolation, cleaning and partial rate cut on 21-May-2026.
RCA & CAPA/PAA | AR-2026-ZCU-0165 | HE-3301 — ZCU

## Slide 3
GENERAL PROCESS OVERVIEW
Chronology of Events
03/11
18-May-2026
Heat-recovery section running; HE-3301 tube-side dP rising (0.4 → 0.9 bar) and cold-outlet temperature falling.
21-May-2026 09:00
Preheat duty dropped ~35% below design; unit rate reduced to protect downstream. Exchanger isolated.
21-May-2026 11:30
Tube bundle inspected — heavy coke/polymer deposition on tube side.
21-May-2026 21:00
Bundle hydro-jet cleaned and returned to service; duty and dP restored, rate ramped back to 30 T/H.
Problem: Feed/Effluent Heat Exchanger HE-3301 suffered accelerated tube-side fouling reducing duty and raising dP, forcing an unplanned isolation, cleaning and partial rate cut on 21-May-2026.
RCA & CAPA/PAA | AR-2026-ZCU-0165 | HE-3301 — ZCU

## Slide 4
ASSESS
Past Performance Analysis
04/11
HISTORICAL DATA & EVIDENCE
HE-3301 tube-side dP baseline is 0.3–0.4 bar; heat duty design 100%. Over the run, dP climbed steadily while duty fell — a classic fouling curve. No dP-based cleaning trigger existed, so fouling was allowed to progress to a forced cut.
IMPACT SUMMARY (4W)
What:
HE-3301 duty loss & high dP from tube-side fouling
When:
21-May-2026 (09:00)
Scope:
Partial rate cut of ZCU heat-recovery section
Uptime Loss:
12.0 hours → 216.0 ton → $183.6k
RCA & CAPA/PAA | AR-2026-ZCU-0165 | HE-3301 — ZCU

## Slide 5
TARGET SETTING
Actual vs Target Condition
05/11
ACTUAL CONDITION (Before Improvement)
Rate cut due to HE-3301 fouling (duty loss + high dP)
TARGET CONDITION (Project Y)
No unplanned rate cut due to HE-3301 fouling (dP < 0.6 bar, duty > 90%)
TARGET METRIC
Recurrence of this equipment failure mode:
Before = 1 case → Target = 0 case
Chart: Failure Case — Before vs Target
| Before | Target
Failure Cases | 1 | 0
RCA & CAPA/PAA | AR-2026-ZCU-0165 | HE-3301 — ZCU

## Slide 6
ROOT CAUSE ANALYSIS
Parameter Verification (4P)
06/11
#
Problem Phenomenon / Parameter
Result
Evidence / Finding
P1
Tube-side dP above limit
NG
dP reached 0.9 bar vs 0.6 bar limit — heavy fouling.
P2
Heat duty below design
NG
Duty fell to ~65% of design — loss of preheat.
P3
Feed heavy-ends above spec
NG
Heavy-ends 2.4% vs < 1.5% design — increased fouling precursor.
P4
Tube velocity below design
G
Tube velocity 1.9 m/s vs 1.5 m/s min — adequate.
P5
Cooling/heating medium temperature off
G
Shell-side inlet temperature within normal band.
NG = current condition not meeting standard (problem) • G = meets standard
RCA & CAPA/PAA | AR-2026-ZCU-0165 | HE-3301 — ZCU

## Slide 7
ROOT CAUSE ANALYSIS
4M + 1E Verification
07/11
#
Man / Machine / Method / Material / Environment
Result
Evidence / Finding
X1
No dP-based cleaning trigger
NG
Cleaning was time-based only; no dP alarm to trigger action.
X2
Feed filtration performance not trended
NG
Upstream filter dP not monitored, allowing heavy-ends carry-over.
X3
Fouling KPI not on dashboard
NG
No fouling factor / duty KPI tracked between TAs.
X4
Bundle metallurgy inadequate
G
Bundle metallurgy suitable for service.
ROOT CAUSE: Accelerated tube-side coke/polymer fouling driven by higher-than-design feed heavy-ends, allowed to progress by the absence of a dP-based cleaning trigger and fouling KPI, causing duty loss, high dP and a forced rate cut.
RCA & CAPA/PAA | AR-2026-ZCU-0165 | HE-3301 — ZCU

## Slide 8
RCA — MATRIX PRIORITY
Impact vs Control Prioritization
08/11
X1 X2 X3
P1 P2 P3
Low
Medium
High
IMPACT →
CONTROL →
Low
Medium
High
Prioritized root causes (high impact) are addressed first via Corrective & Pro-Active Actions →
RCA & CAPA/PAA | AR-2026-ZCU-0165 | HE-3301 — ZCU

## Slide 9
IMPROVE
Corrective & Pro-Active Action (CAPAA)
09/11
RC
Corrective Action
Plan Date
PIC
Status
X1
Add dP-based cleaning trigger & alarm for HE-3301
22-Jun-2026
STA-02
In Progress
P3
Tighten feed heavy-ends control & filtration
30-Jun-2026
ROT-01
Open
PRO-ACTIVE ACTION (roll-out to similar equipment)
RC
Pro-Active Action
Plan Date
PIC
Status
X1
Apply dP-trigger logic to parallel exchangers HE-3302/3303
22-Jul-2026
STA-02
Open
P3
Review upstream fractionation cut-point control
31-Jul-2026
ROT-01
Open
RCA & CAPA/PAA | AR-2026-ZCU-0165 | HE-3301 — ZCU

## Slide 10
IMPROVE
Preventive & Risk Analysis
10/11
PREVENTIVE / PRO-ACTIVE ACTION (Good Condition Parameters)
Item
Possible Root Cause
Preventive Action
Plan Date
PIC
X3
No fouling KPI
Add fouling factor & duty KPI to reliability dashboard
22-Jun-2026
STA-02
X2
Filter not trended
Add upstream filter dP trend & replacement trigger
30-Jun-2026
ROT-01
RISK ANALYSIS OF CORRECTIVE ACTION
Corrective Action
Potential Risk
Countermeasure
Plan Date
PIC
Add dP cleaning trigger
Premature/over-frequent cleaning
Set trigger with hysteresis + engineering review before cleaning
22-Jun-2026
STA-02
PM SCHEDULE ESTABLISHED
PM No.
Description
Group
Interval
PM-1
Daily HE-3301 dP & duty trend review
Process
Daily
PM-2
Bundle inspection & cleaning at dP trigger / next TA
Static
Condition / TA
RCA & CAPA/PAA | AR-2026-ZCU-0165 | HE-3301 — ZCU

## Slide 11
Downtime & Closure Summary
DOWNTIME
12.0 h
PRODUCTION LOSS
216.0 ton
ESTIMATED LOSS
$183.6k
PRE-RISK
III (400)
ROOT CAUSE
Accelerated tube-side coke/polymer fouling driven by higher-than-design feed heavy-ends, allowed to progress by the absence of a dP-based cleaning trigger and fouling KPI, causing duty loss, high dP and a forced rate cut.
KEY CORRECTIVE / PRO-ACTIVE ACTIONS
• Add dP-based cleaning trigger & alarm for HE-3301
• Tighten feed heavy-ends control & filtration
• Add fouling factor & duty KPI to reliability dashboard
AR-2026-ZCU-0165 • HE-3301 — ZCU