## Slide 1
ABNORMALITY REPORT — RCA & CAPA/PAA
Equipment Related Risk
Product Blower BL-5702
High Vibration (Coupling Misalignment)
AR NUMBER
AR-2026-OPP-0203
TAG / PLANT
BL-5702 | OPP
DATE OCCURRENCE
17 Jun 2026
PRE-RISK
III (Score 400)
PIC (RCA)
ROT-01
Procedure No. RCA-P-0050-03 • Form RCA-F-0075-02

## Slide 2
PROBLEM IDENTIFICATION
AR Details & Problem Statement
02/11
AR IDENTIFICATION
Title / Problem
Product Blower BL-5702 — High Vibration (Coupling Misalignment)
AR Type
OPEDR (Operation) — Uptime
Plant / Unit
OPP (Orion Polypropylene Plant)
Tag / Eq. Class
BL-5702 | Class A
Discipline
ROT
Date Occurrence
17 Jun 2026
Date Reported
18 Jun 2026
Immediate Action
Stop BL-5702, re-align coupling, replace worn coupling element
SEVERITY
Major
PRE-RISK
III
DOWNTIME
14.0 h
LOSS
$478.8k
PROBLEM STATEMENT
Product Blower BL-5702 tripped on high vibration on 17-Jun-2026 due to coupling misalignment and a worn coupling element, halting the OPP powder-handling section.
RCA & CAPA/PAA | AR-2026-OPP-0203 | BL-5702 — OPP

## Slide 3
GENERAL PROCESS OVERVIEW
Chronology of Events
03/11
15-Jun-2026
OPP running normal; BL-5702 vibration trending up (4.2 → 8.5 mm/s) with 2X harmonic rising.
17-Jun-2026 04:30
BL-5702 vibration reached alarm (11 mm/s); blower stopped to prevent damage — powder handling section halted.
17-Jun-2026 07:00
Coupling element found worn/cracked; laser alignment showed 0.35 mm offset (spec < 0.05 mm).
17-Jun-2026 18:30
Coupling element replaced, unit re-aligned to < 0.05 mm, blower restarted to 38 T/H.
Problem: Product Blower BL-5702 tripped on high vibration on 17-Jun-2026 due to coupling misalignment and a worn coupling element, halting the OPP powder-handling section.
RCA & CAPA/PAA | AR-2026-OPP-0203 | BL-5702 — OPP

## Slide 4
ASSESS
Past Performance Analysis
04/11
HISTORICAL DATA & EVIDENCE
BL-5702 vibration baseline is 3.5–4.5 mm/s. A rising trend with dominant 2X harmonic over 2 days indicated developing misalignment. Alignment was last verified 14 months prior; no soft-foot / alignment check in the routine PM.
IMPACT SUMMARY (4W)
What:
BL-5702 high vibration from coupling misalignment
When:
17-Jun-2026 (04:30)
Scope:
OPP powder-handling section stop
Uptime Loss:
14.0 hours → 532.0 ton → $478.8k
RCA & CAPA/PAA | AR-2026-OPP-0203 | BL-5702 — OPP

## Slide 5
TARGET SETTING
Actual vs Target Condition
05/11
ACTUAL CONDITION (Before Improvement)
Blower stop due to high vibration (misalignment)
TARGET CONDITION (Project Y)
No blower stop due to misalignment (vibration < 7 mm/s, alignment < 0.05 mm)
TARGET METRIC
Recurrence of this equipment failure mode:
Before = 1 case → Target = 0 case
Chart: Failure Case — Before vs Target
| Before | Target
Failure Cases | 1 | 0
RCA & CAPA/PAA | AR-2026-OPP-0203 | BL-5702 — OPP

## Slide 6
ROOT CAUSE ANALYSIS
Parameter Verification (4P)
06/11
#
Problem Phenomenon / Parameter
Result
Evidence / Finding
P1
Overall vibration above alarm
NG
Vibration reached 11 mm/s vs 7 mm/s alarm — misalignment signature.
P2
Coupling alignment out of tolerance
NG
Offset 0.35 mm vs < 0.05 mm spec — angular/parallel misalignment.
P3
Bearing condition degraded
G
Bearing envelope/shock-pulse normal — no bearing defect.
P4
Foundation / soft-foot
NG
Soft-foot 0.12 mm found on one foot — contributed to misalignment.
P5
Rotor unbalance
G
1X component within balance grade — no unbalance.
NG = current condition not meeting standard (problem) • G = meets standard
RCA & CAPA/PAA | AR-2026-OPP-0203 | BL-5702 — OPP

## Slide 7
ROOT CAUSE ANALYSIS
4M + 1E Verification
07/11
#
Man / Machine / Method / Material / Environment
Result
Evidence / Finding
X1
Alignment check not in routine PM
NG
PM did not include periodic laser alignment / soft-foot check.
X2
Coupling element life not tracked
NG
Elastomer coupling element run beyond recommended 12-month life.
X3
Vibration route interval too long
NG
Monthly route missed the fast-rising 2-day trend.
X4
Alignment tools / competency
G
Laser alignment tool & trained technicians available.
ROOT CAUSE: High vibration from coupling misalignment aggravated by soft-foot and an over-aged elastomer coupling element, undetected because periodic alignment/soft-foot checks were absent from the PM and the vibration route interval was too long.
RCA & CAPA/PAA | AR-2026-OPP-0203 | BL-5702 — OPP

## Slide 8
RCA — MATRIX PRIORITY
Impact vs Control Prioritization
08/11
X1 X2 X3
P1 P2 P4
Low
Medium
High
IMPACT →
CONTROL →
Low
Medium
High
Prioritized root causes (high impact) are addressed first via Corrective & Pro-Active Actions →
RCA & CAPA/PAA | AR-2026-OPP-0203 | BL-5702 — OPP

## Slide 9
IMPROVE
Corrective & Pro-Active Action (CAPAA)
09/11
RC
Corrective Action
Plan Date
PIC
Status
X1
Add periodic laser alignment & soft-foot check to BL-5702 PM
18-Jul-2026
ROT-01
In Progress
X2
Track coupling element life & replace at 12 months
18-Jul-2026
REL-05
Open
PRO-ACTIVE ACTION (roll-out to similar equipment)
RC
Pro-Active Action
Plan Date
PIC
Status
X1
Roll out alignment check to all Class-A blowers in OPP
18-Aug-2026
ROT-01
Open
X2
Create coupling-element replacement register for OPP trains
31-Aug-2026
REL-05
Open
RCA & CAPA/PAA | AR-2026-OPP-0203 | BL-5702 — OPP

## Slide 10
IMPROVE
Preventive & Risk Analysis
10/11
PREVENTIVE / PRO-ACTIVE ACTION (Good Condition Parameters)
Item
Possible Root Cause
Preventive Action
Plan Date
PIC
X3
Route interval too long
Shorten BL-5702 vibration route to weekly
18-Jul-2026
REL-05
P4
Soft-foot
Correct soft-foot & re-shim baseplate BL-5702
18-Jun-2026
ROT-01
RISK ANALYSIS OF CORRECTIVE ACTION
Corrective Action
Potential Risk
Countermeasure
Plan Date
PIC
Shorten vibration route to weekly
Increased inspection workload
Use wireless vibration sensor for continuous trend
18-Jul-2026
REL-05
PM SCHEDULE ESTABLISHED
PM No.
Description
Group
Interval
PM-1
6-monthly laser alignment & soft-foot check BL-5702
Rotating
6-monthly
PM-2
Coupling element inspection/replacement
Rotating
12-monthly
PM-3
Weekly vibration trend review BL-5702
Reliability
Weekly

## Slide 11
Downtime & Closure Summary
DOWNTIME
14.0 h
PRODUCTION LOSS
532.0 ton
ESTIMATED LOSS
$478.8k
PRE-RISK
III (400)
ROOT CAUSE
High vibration from coupling misalignment aggravated by soft-foot and an over-aged elastomer coupling element, undetected because periodic alignment/soft-foot checks were absent from the PM and the vibration route interval was too long.
KEY CORRECTIVE / PRO-ACTIVE ACTIONS
• Add periodic laser alignment & soft-foot check to BL-5702 PM
• Track coupling element life & replace at 12 months
• Shorten BL-5702 vibration route to weekly
AR-2026-OPP-0203 • BL-5702 — OPP